## Slide 1: CMSC 449/691 Malware Analysis
Lecture 7
x86 Assembly revised Spring 2025

## Slide 2: General Purpose Registers
EAX
EBX
ECX
EDX
(AL, AH, AX)
(BL, BH, BX)
(CL, CH, CX)
(DL, DH, DX)
Stores return value
Loop counter
Used with EAX in multiplication, division

## Slide 3: More General Purpose Registers
ESI
EDI
ESP
EBP
Source pointer
Destination pointer
Stack pointer
Base pointer

## Slide 4: Other Registers
EIP
EFLAGS
  ZF
  CF
  OF
Instruction pointer
Status register
Zero Flag
Carry Flag
Overflow Flag

## Slide 5: MOV
MOV EAX, EBX
MOV EAX, 0x0
MOV EAX, dword ptr [0x400000]
MOV EAX, dword ptr [EBX + ESI * 4]

## Slide 6: LEA
“Load Effective Address”
Moves a pointer into a register, does not dereference
LEA EAX, [EBX + 8]
  Puts EBX + 8 into EAX
MOV EAX, dword ptr [EBX + 8]
  Dereferences EBX + 8 and puts value into EAX

## Slide 7: Arithmetic Instructions
ADD EAX, 0x10
SUB EAX, EBX
INC EAX
DEC EAX

## Slide 8: More Arithmetic Instructions
MOV EAX, 0x2 Multiples EAX by 4, stores upper 32 MUL 0x4 bits in EDX and lower 32 bits in EAX
MOV EDX, 0x0 Divides EDX:EAX by 3, stores MOV EAX, 0x9 result in EAX and remainder in EDX DIV 0x3

## Slide 9: Logical Operator Instructions
XOR EAX, EAX
AND EAX, 0xFF
OR EAX, EBX

## Slide 10: Bit Shifting Instructions
SHL EAX, 0x2
SHR EAX, EBX
ROL EAX, 0x4
ROR EAX, EBX
Notes: SHR rightmost bit stored in carry flag
SAR restores MSB
SHL and SAL are the same
RCL and RCR also use the carry flag

## Slide 11: Conditional Instructions
CMP EAX, EBX
TEST EAX, 0x10
TEST EAX, EAX
Notes: Test - performs bitwise and on two operands, so the reason you see TEST EAX, EAX is because it sets the zero flag to one, which allows you to jump
CMP - actually does subtraction sets flags according to result, why if zero they’re equal

## Slide 12: Branching Instructions
JMP LOC Unconditional jump
JZ / JE LOC Jump if ZF == 1
JNZ / JNE LOC Jump if ZF == 0
JG / JA LOC Jump if DST > SRC
JL / JB LOC Jump if DST < SRC
JGE / JAE LOC Jump if DST >= SRC
JLE / JBE LOC Jump if DST <= SRC

## Slide 13: REP Instructions
Used for making common loop constructions more efficient
  Increment ESI and EDI pointers, decrement ECX in a loop
REP (Repeat) Stops when ECX = 0
REPE (Repeat while ==) Stops when ECX = 0 or ZF = 0
REPNE (Repeat while !=) Stops when ECX = 0 or ZF = 1

## Slide 14: Common REP Instructions
REPE CMPSB Compare ESI and EDI buffers
REP STOSB Initialize all bytes of EDI buffer to the value stored in AL
REP MOVSB Copy contents of ESI to EDI
REPNE SCASB Search EDI for the byte in AL

## Slide 15: PUSH in Assembly Language
What does PUSH actually do?
PUSH myVal
  SUB ESP, 4
  MOV dword ptr [ESP], myVal
Subtract 4 from the stack pointer (“make room” on the stack)
Copy the value into that new space on the stack

## Slide 16: POP in Assembly Language
What does POP actually do?
POP myRegister
  MOV myRegister, dword ptr [ESP]
  ADD ESP, 4
Add 4 to the stack pointer (move the stack back “up”)
Copy the value off the stack into the register

## Slide 17: CALL in Assembly Language
What does CALL actually do?
CALL myFunc
  PUSH &nextInstruction
    SUB ESP, 4
    MOV dword ptr [ESP], &nextInstruction
  JMP myFunc
Jump to where the function you’re calling resides in memory
Push the address in memory you’ll want to return to

## Slide 18: RET in Assembly Language
What does RET actually do?
RET
  POP EIP
Trusting that whatever’s at the top of the stack is the return address
  When you execute the next instruction it looks at EIP to see what to do next
Pop the return address into EIP